## Slide 1: Multilevel Streaming for Out-of-Core Surface Reconstruction
Matthew Bolitho, Michael Kazhdan, Randal Burns, Hugues Hoppe

## Slide 2: Motivation
With improvements in acquisition technology, huge datasets are now available for processing.
USGS Earth: 2.2x1010 Points
UVA Monticello: 2.0x107 Points
XYZRGB Thai Statue: 3.4x107 Points
Stanford St. Mathew: 1.8x108 Points

## Slide 3: Motivation
With improvements in acquisition technology, huge datasets are now available for processing.
USGS Earth: 2.2x1010 Points
UVA Monticello: 2.0x107 Points
XYZRGB Thai Statue: 3.4x107 Points
Stanford St. Mathew: 1.8x108 Points
Some of these models have becomes so large that it is hard to maintain the dataset (let alone data-structure) in working memory.

## Slide 4: Streaming Approaches
If a traversal order is defined and the data is sorted, stream through the data:
  Processing data at the current position using only the data in the working set
  When advancing the stream, reading into the head of the working set and writing out the tail.

## Slide 5: Streaming Approaches
If a traversal order is defined and the data is sorted, stream through the data:
  Processing data at the current position using only the data in the working set
  When advancing the stream, reading into the head of the working set and writing out the tail.
Locality of processing implies that the size of the working set remains small.

## Slide 6: Streaming Approaches
If the processing is local, the algorithm may be implemented in a streaming framework:
  Define a traversal ordering on the data
  Stream through the data
    Process data at the current stream position using only the data in the current working set
    When advancing the stream, update the head of the working set and release the tail.
Locality of processing implies that the size of the working set remains small.
Pajarola, 2005

## Slide 7: Streaming Approaches
A number of mesh processing applications are local and are well-suited for streaming implementations:
  Simplification [Wu and Kobbelt, 2003]
  Compression [Isenberg and Gumhold, 2003]
  Smoothing [Pajarola, 2005]
  Re-Meshing [Anh et al. 2006]

## Slide 8: Surface Reconstruction
In general, scanners return samples (or local patches) from a 3D surface and one of the first steps to be performed is reconstruction.
Scanned Data Point Samples
Reconstructed Model Triangle Mesh

## Slide 9: Outline
Introduction
Streaming Surface Reconstruction
  Octree-Based Poisson Reconstruction
  Streaming the Octree
  Streaming the Reconstruction
Results
Conclusion

## Slide 10: In-Core Reconstruction
Reconstruction can be reduced to solving a Poisson equation [Kazhdan et al. 06]:
  Reconstruct by solving for the indicator function.
Indicator function
0
1
0
0
0
0
1
1
M

## Slide 11: In-Core Reconstruction
Reconstruction can be reduced to solving a Poisson equation [Kazhdan et al. 06]:
  Reconstruct by solving for the indicator function.
  Oriented points sample the gradient of the function.
M
Indicator gradient
0
0
0
0
0
0
Oriented points

## Slide 12: In-Core Reconstruction
Reconstruction can be reduced to solving a Poisson equation [Kazhdan et al. 06]:
  Reconstruct by solving for the indicator function.
  Oriented points sample the gradient of the function.
  Solve for the function  whose gradient best approximates the surface samples V:

## Slide 13: In-Core Reconstruction
Reconstruction can be reduced to solving a Poisson equation [Kazhdan et al. 06]:
  Reconstruct by solving for the indicator function.
  Oriented points sample the gradient of the function.
  Solve for the function  whose gradient best approximates the surface samples V:

## Slide 14: In-Core Reconstruction
Reconstruction can be reduced to solving a Poisson equation [Kazhdan et al. 06]:
  Extend oriented samples to vector field
  Compute divergence
  Solve Poisson equation
  Extract isosurface
(1)
(2)
(3)
(4)

## Slide 15: In-Core Reconstruction
Advantages
  Reconstruction as a global problem:
    The solution is resilient to noise
  Poisson system over an octree:
    Storage adapted to surface complexity
(1)
(2)
(3)
(4)

## Slide 16: In-Core Reconstruction
To extend Poisson reconstruction to a streaming context:
  Representation: We need a data-structure allowing for streaming through an octree
  Implementation: We need to implement Poisson reconstruction as a local system

## Slide 17: Streaming the Octree
Motivation (Regular Grid):
We can store the grid on disk as a set of successive pixel columns.

## Slide 18: Streaming the Octree
Motivation (Regular Grid):
We can stream across the x-axis, reading/writing successive blocks.
x=0

## Slide 19: Streaming the Octree
Motivation (Regular Grid):
We can stream across the x-axis, reading/writing successive blocks.
x=1

## Slide 20: Streaming the Octree
Motivation (Regular Grid):
We can stream across the x-axis, reading/writing successive blocks.
x=2

## Slide 21: Streaming the Octree
Challenge:
In the case of an octree, nodes at different depths persist for different time-spans.
x=x0
x=x0+1

## Slide 22: Streaming the Octree
Solution:
To manage depth-related-persistence, we define a separate stream for each depth.
Octree
Data Streams
d=0 d=1
d=2
d=3
d=4
d=5

## Slide 23: Streaming the Octree
Solution:
To manage depth-related-persistence, we define a separate stream for each depth.
Data Streams
d=0 d=1
d=2
d=3
d=4
d=5
Octree

## Slide 24: Streaming the Octree
Solution:
To manage depth-related-persistence, we define a separate stream for each depth.
Data Streams
d=0 d=1
d=2
d=3
d=4
d=5
Octree

## Slide 25: Streaming the Octree
Solution:
To manage depth-related-persistence, we define a separate stream for each depth.
Data Streams
d=0 d=1
d=2
d=3
d=4
d=5
Octree

## Slide 26: Streaming the Octree
Solution:
To manage depth-related-persistence, we define a separate stream for each depth.
Data Streams
d=0 d=1
d=2
d=3
d=4
d=5
Octree

## Slide 27: Streaming the Octree
Solution:
We can manage node persistence by advancing through the streams at different speeds.

## Slide 28: Streaming the Octree
Solution:
We can manage node persistence by advancing through the streams at different speeds.
For an octree of height h:
Resolution: R=2h
Octree Size: O(R2)
Octree in Working Memory: O(R)

## Slide 29: Streaming the Reconstruction
We must implement the reconstruction in a streaming fashion.
  Extend oriented samples to vector field
  Compute divergence
  Solve Poisson equation
  Extract isosurface
(1)
(2)
(3)
(4)

## Slide 30: Streaming the Reconstruction
We must implement the reconstruction in a streaming fashion.
  Extend oriented samples to vector field
  Compute divergence
  Solve Poisson equation
  Extract isosurface
(1)
(2)
(3)
(4)

## Slide 31: Streaming the Reconstruction
We must implement the reconstruction in a streaming fashion.
  Extend oriented samples to vector field
  Compute divergence
  Solve Poisson equation
  Extract isosurface
(1)
(2)
(3)
(4)
Solving a Poisson system is not a local process!

## Slide 32: Streaming the Reconstruction
Reconstruction Locality:
Using iterative update methods, the Poisson system can be solved in a local manner.

## Slide 33: Streaming the Reconstruction
Reconstruction Locality:
Using iterative update methods, the Poisson system can be solved in a local manner.
>2500 Jacobi Iterations

## Slide 34: Streaming the Reconstruction
Reconstruction Efficiency:
Using cascadic multigrid, the system can be solved efficiently in a local manner:
  The solution is obtained by solving at coarser depths and updating/initializing the equation at finer depths.
  Within each depth, we use a Jacobi solver to update the solution coefficients in the working set.

## Slide 35: Streaming the Reconstruction
Reconstruction Efficiency:
Using cascadic multigrid, the system can be solved efficiently in a local manner:
  The solution is obtained by solving at coarser depths and updating/initializing the equation at finer depths.
  Within each depth, we use a Jacobi solver to update the solution coefficients in the working set.
One pass suffices for an accurate solution!

## Slide 36: Streaming the Reconstruction
Implementation:
High-res solutions trail the low-res solutions.
A single pass suffices for accurate reconstruction.

## Slide 37: Outline
Introduction
Streaming Surface Reconstruction
Results
Conclusion

## Slide 38: David (Complexity)
Res. | Octree Memory | Peak Memory | Running Time
256 | 48 | 521 | 0.53
512 | 168 | 278 | 0.68
1024 | 702 | 213 | 1.20
2048 | 3,070 | 212 | 3.33
4096 | 13,367 | 427 | 12.6
8192 | 39,452 | 780 | 32.3
Out-of-Core Reconstruction
216x106 points (4.8 GB)

## Slide 39: David (Complexity)
Res. | Octree Memory | Peak Memory | Running Time
256 | 48 49 | 521 309 | 0.53 0.50
512 | 168 188 | 278 442 | 0.68 0.65
1024 | 702 818 | 213 1,285 | 1.20 1.05
2048 | 3,070 3,695 | 212 4,442 | 3.33 2.65
4096 | 13,367 N/A | 427 N/A | 12.6 N/A
8192 | 39,452 N/A | 780 N/A | 32.3 N/A
Out-of-Core Reconstruction
In-Core Reconstruction
216x106 points (4.8 GB)

## Slide 40: David (Comparison)
Out-of-Core Reconstruction Peak Mem: 0.8 GB
In-Core Reconstruction
Peak Mem: 4.4 GB

## Slide 41: Outline
Introduction
Streaming Surface Reconstruction
Results
Conclusion

## Slide 42: Conclusion
Methodology:
We have presented a multilevel streaming framework for out-of-core processing of octrees
Octree
Data Streams
d=0 d=1
d=2
d=3
d=4
d=5

## Slide 43: Conclusion
Application:
We have implemented streaming surface reconstruction in three passes through the data.

## Slide 44: Conclusion
We can reconstruct watertight surface using a memory footprint smaller than:
  The total memory used
  The size of the input point set
  The size of the output surface
Points (391x106) Triangles (431x106) Total Memory | 9.8 GB 7.8 GB 106 GB | 
Working Memory |  | 2 GB

## Slide 45: Conclusion
We can reconstruct watertight surface using a memory footprint smaller than:
  The total memory used
  The size of the input point set
  The size of the output surface
Points (391x106) Triangles (431x106) Total Memory | 9.8 GB 7.8 GB 106 GB | 
Working Memory |  | 2 GB

## Slide 46: Conclusion
We can reconstruct watertight surface using a memory footprint smaller than:
  The total memory used
  The size of the input point set
  The size of the output surface
Points (391x106) Triangles (431x106) Total Memory | 9.8 GB 7.8 GB 106 GB | 
Working Memory |  | 2 GB

## Slide 47: Conclusion
We can reconstruct watertight surface using a memory footprint smaller than:
  The total memory used
  The size of the input point set
  The size of the output surface
Points (391x106) Triangles (431x106) Total Memory | 9.8 GB 7.8 GB 106 GB | 
Working Memory |  | 2 GB

## Slide 48: Conclusion
We can reconstruct watertight surface using a memory footprint smaller than:
  The total memory used
  The size of the input point set
  The size of the output surface
…
Points (391x106) Triangles (431x106) Total Memory | 9.8 GB 7.8 GB 106 GB | 
Working Memory |  | 2 GB

## Slide 49: Thank You!
http://www.cs.jhu.edu/~misha/Code/OOCReconstruction http://www.cs.jhu.edu/~bolitho/Research/StreamingSurfaceReconstruction